## Slide 1: CCV project file March 19 2010

## Slide 2: Step1 : Customization
Open CCVProjectFile CATProduct, located in :
Intel_a\startup\Tooling\CCV\ProjectFile
Modify it as needed. For instance
  - you may remove the analysis in « model with compensation » if you do not need them
  - you may put your own database of materials in the excel file
  -you may change the parameter names ..
Use SaveManagement to save your customized project file. You will re use it at the start of all new projects.

## Slide 3: Step 2 :Settings
Check the update options in Tools/Option
Mechanical Design\AssemblyDesign
ProductStructure\ PartInfrastructure
and make sure they correspond to what you want

## Slide 4: Step 3 : receiving a customer part
Make sure the solid model representing the model in the customer part is published with name « ReferenceModel »
Make sure the right axis system is published with the name « ModelAxisSystem » : it is used to apply the stretch factors ( compensation )
The customer part is not be modified by these two publications

## Slide 5: Step 4 : Using the CCV project file
Open your CCVProjectFile and save it in a folder associated to your new customer part (save management )
Replace the component « ReferenceModel » by your customer part ( ASD command )
Update the entire structure at the assembly and part levels.
Save everything ( save management )

## Slide 6: Step 5 : Part « Model with compensation »
In this Part, a certain number of properties and analysis are already pre computed ( by associativity )
The compensation has been applied ( you may change the material , the stretch factors will be automatically modified and applied )
It is possible to report such information to the customer.

## Slide 7: Step 6 : ManufacturingPart
The manufacturing part is the part dedicated to preparation of the tool surfaces and mechanisms.
The customer model ( stretched) is already copied into this part.
A convenient structure of bodies and geometrical sets is prepared
The key publications are prepared but they point on dummy geometry.
This dummy geometry needs to be replaced by you with the corresponding geometry on your customer part.

## Slide 8: Step 67: ManufacturingPart
If you open the manufacturing part in a new window, you may enhance the structure by just specifying how many sliders and lifters you need.